MATHEMATICS
CALCULUS

---
Differential Equations
Part – 3

---
Methods of solving a Differential Equation
Homogeneous Differential Equations:
If the degree of each term is same in a diffrential equation then the
equation is called ahomogeneous Differetial Equation.
To solve the homogeneous differential equation, we use the substitution
Linear Differential Equations:
The differential equation of the type,
are constants or functions of only is called Linear Differential
       Equation (LDE). To find the solution of the LDE, multiply the equation
by the Integrating Factor (IF) throughout then we get ,
y = ux \text { and replace } \frac{dy}{dx} = u + x\frac{du}{dx}
\frac{dy}{dx} + Py = Q \ \ \text { where } P \text { and } Q
x
= e^{\int P\ dx}

---
e^{\int P dx}\left[ \frac{dy}{dx} + Py \right] = Q e^{\int P dx}
\frac{d}{dx} \left[ y.e^{\int P dx} \right] = Q e^{\int P dx}
\left[\ \text {Note : } \frac{d}{dx} \left( y.e^{\int P dx} \right) = e^{\int P dx}\left( \frac{dy}{dx} + Py \right) \ \right]
\text {Integrating both the sides we get,}
y.e^{\int P dx} = \int Q e^{\int P dx} dx
\text {In general we can say, the general solution is }
y.\text {( I.F. )} = \int Q \text {( I.F. )} dx
\text {For the LDE of the type } \ \frac{dx}{dy} + Px = Q
x.\text {( I.F. )} = \int Q \text {( I.F. )} dy
\text {the general solution is }

---
Examples
\text {Solve the following differential equations .}
\text {(i) } y^2 dx + ( xy + x^2 ) dy = 0
\text {(1)}
\text {(iii) } x dy + 2ydx = 0 \text { when } x = 2, \ y = 1.
\text {Solutions : }
\text {(i). Given that, } y^2 dx + ( xy + x^2 ) dy = 0
.\ .\ .\ \ \ \text {(1)}
\text {(ii) } y^2 - x^2 \frac{dy}{dx} = xy \frac{dy}{dx}
\text {(iv) } ( x^2 + 3xy + y^2 )dx - x^2 dy = 0
\text {(v)} \left( 1 + e^{ \frac{x}{y} } \right) dx + e^{ \frac{x}{y} }\left( 1 - \frac{x}{y} \right) dy = 0
\text {(vi) } x \frac{dy}{dx} - y + x \sin \left( \frac{y}{x} \right) = 0
( xy + x^2 ) dy = - y^2 dx
\therefore \ \ \frac{dy}{dx} = - \frac{y^2}{xy + x^2}

---
\therefore \ \ \frac{dy}{dx} = u + x \frac{du}{dx}
\text {Put } y = ux
\text {Diff. } w. \ r. \ t. \ x
.\ .\ .\ \ \ \text {(2)}
\text {From (1), (2) and (3) we get, }
u + x \frac{du}{dx} = - \frac{u^2 x^2}{x(ux) + x^2} = - \frac{u^2 x^2}{ux^2 + x^2}
u + x \frac{du}{dx} = - \frac{u^2 x^2}{x^2( u + 1 ) }
x \frac{du}{dx} = - \frac{u^2 }{ u + 1 } - u
\Rightarrow \ \ x \frac{du}{dx} = - \left[ \frac{u^2 + u^2 + u }{ u + 1 } \right]
\Rightarrow \ \ x \frac{du}{dx} = - \frac{2u^2 + u }{ u + 1 }
.\ .\ .\ \ \ \text {(3)}

---
\therefore \ \ \frac{u + 1}{2u^2 + u } du = - \frac{1}{ x } dx
\text {Integrating throughout, we get, }
\int \frac{u + 1}{2u^2 + u } du = - \int \frac{1}{ x } dx
\int \frac{ ( 2u + 1 ) - u }{u ( 2u + 1 ) } du = - \int \frac{1}{ x } dx
\int \left[ \frac{1}{u} - \frac{1}{ 2u + 1 } \right] du = - \int \frac{1}{ x } dx
\log u - \frac{1}{2} \log ( 2u + 1 ) = - \log x + \log c
2\log u - \log ( 2u + 1 ) = 2\log c - 2\log x
\log u^2 - \log ( 2u + 1 ) = \log c^2 - \log x^2

---
\text {i.e.}
\log \left( \frac{u^2}{2u + 1} \right) = \log \left( \frac{c^2}{ x^2} \right)
\text {i.e.}
\frac{u^2}{2u + 1} = \frac{c^2}{ x^2}
\text {is the required general solution.}
\text {(ii). } y^2 - x^2 \frac{dy}{dx} = xy \frac{dy}{dx}
.\ .\ .\ \ \ \text {(1)}
\therefore \ \ \frac{dy}{dx} = \frac{y^2}{xy + x^2}
\frac{\frac{y^2}{x^2}}{ \frac{2y}{x} + 1} = \frac{c^2}{ x^2}
\Rightarrow
\frac{\frac{y^2}{x^2}}{ \frac{2y + x}{x}} = \frac{c^2}{ x^2}
\Rightarrow
\text {i.e.}
xy^2 = c^2(x + 2y)
y^2 = x^2 \frac{dy}{dx} + xy \frac{dy}{dx}
y^2 = ( x^2 + xy ) \frac{dy}{dx}
\Rightarrow
.\ .\ . \ \text {[ From (2) ]}

---
\therefore \ \ \frac{dy}{dx} = u + x \frac{du}{dx}
\text {Put } y = ux
\text {Diff. } w. \ r. \ t. \ x
.\ .\ .\ \ \ \text {(2)}
\text {From (1), (2) and (3) we get, }
u + x \frac{du}{dx} = \frac{u^2 x^2}{x(ux) + x^2} = \frac{u^2 x^2}{ux^2 + x^2}
u + x \frac{du}{dx} = \frac{u^2 x^2}{x^2( u + 1 ) }
x \frac{du}{dx} = \frac{u^2 }{ u + 1 } - u
\Rightarrow \ \ x \frac{du}{dx} = \frac{u^2 - u^2 - u }{ u + 1 }
.\ .\ .\ \ \ \text {(3)}
\Rightarrow \ \ x \frac{du}{dx} = - \frac{ u }{ u + 1 }

---
\therefore \ \ \frac{u + 1}{ u } du = - \frac{1}{ x } dx
\text {Integrating throughout, we get, }
\int \frac{u + 1}{ u } du = - \int \frac{1}{ x } dx
\int \left[ 1 + \frac{1}{u} \right] du = - \int \frac{1}{ x } dx
u + \log u = - \log x + \log c
u + \log ( u x ) = \log c
y + x\log y = x\log c
\int du + \int \frac{1}{u} du = - \int \frac{1}{ x } dx
u + \log u + \log x = \log c
\Rightarrow
\frac{y}{x} + \log y = \log c
\Rightarrow
\text {is the required general solution.}
.\ .\ . \ \text {[ From (2) ]}

---
\text {(iii). } x dy + 2ydx = 0
.\ .\ .\ \ \ \text {(1)}
x dy = - \ 2ydx
\frac{dy}{dx} = - \frac{2y}{x}
\Rightarrow
\therefore \ \ \frac{dy}{dx} = u + x \frac{du}{dx}
\text {Put } y = ux
\text {Diff. } w. \ r. \ t. \ x
.\ .\ .\ \ \ \text {(2)}
\text {From (1), (2) and (3) we get, }
u + x \frac{du}{dx} = - \frac{2ux}{x}
.\ .\ .\ \ \ \text {(3)}
= - 2u
x \frac{du}{dx} = - 3u
\Rightarrow
\frac{du}{u} = - \frac{3dx}{x}
\text {Integrating throughout, we get, }

---
\int \frac{1}{u} du = - 3 \int \frac{1}{x}dx
\log u = - 3 \log x + \log c
\log u = \log c - \log x^3
\log u = \log \left( \frac{c}{x^3} \right)
\log u = \log \left( \frac{c}{x^3} \right)
\Rightarrow
u = \frac{c}{x^3}
\therefore
\frac{y}{x} = \frac{c}{x^3}
\therefore
x^2y = c
\therefore
.\ .\ . \ \text {[ From (2) ]}
.\ .\ .\ \ \ \text {(4)}
\text {Given that when } x = 2, \ y = 1
\therefore \ \text {from (4), we get}
(4)(1) = c \ \ \Rightarrow \ \ c = 4
\text {put }c = 4 \ \text { in (4) we get }
x^2 y = 4
\text {is the required particular solution.}
\text {is the required general solution.}

---
\text {(iv). } ( x^2 + 3xy + y^2 )dx - x^2 dy = 0
.\ .\ .\ \ \ \text {(1)}
( x^2 + 3xy + y^2 )dx = x^2 dy
\frac{dy}{dx} = \frac{x^2 + 3xy + y^2}{x^2}
\text {i.e.}
\therefore \ \ \frac{dy}{dx} = u + x \frac{du}{dx}
\text {Put } y = ux
\text {Diff. } w. \ r. \ t. \ x
.\ .\ .\ \ \ \text {(2)}
\text {From (1), (2) and (3) we get, }
u + x \frac{du}{dx} = \frac{x^2 + 3x^2u + x^2u^2}{x^2}
.\ .\ .\ \ \ \text {(3)}

---
u + x \frac{du}{dx} = \frac{x^2 ( 1 + 3u + u^2 ) }{x^2}
u + x \frac{du}{dx} = 1 + 3u + u^2
x \frac{du}{dx} = u^2 + 2u + 1
x \frac{du}{dx} = ( u + 1 )^2
\text {i.e.}
\therefore \ \ \frac{du}{( u + 1 )^2 } = \frac{dx}{x}
\text {Integrating throughout, we get, }
\int \frac{1}{ ( u + 1 )^2 } du = \int \frac{1}{x}dx
\int ( u + 1 )^{-2}} du = \int \frac{1}{x}dx

---
\frac{( u + 1 )^{-1}}{-1} = \log x + c_1
- \frac{1}{ u + 1 } = \log x + c_1
- \frac{1}{ \frac{y}{x} + 1 } = \log x + c_1
.\ .\ . \ \text {[ From (2) ]}
\text {i.e.}
- \frac{x}{ y + x } = \log x + c_1
\text {i.e.}
- \log x - \frac{x}{ y + x } = c_1
\log x + \frac{x}{ x + y } = - c_1
\log x + \frac{x}{ x + y } = c
\text {is the required general solution.}
\text {[ where }c = -c_1 \text { ]}

---
\text {(v). } \left( 1 + e^{ \frac{x}{y} } \right) dx + e^{ \frac{x}{y} }\left( 1 - \frac{x}{y} \right) dy = 0
.\ .\ .\ \ \ \text {(1)}
\therefore \ \ \frac{dx}{dy} = u + y \frac{du}{dy}
\text {Put } \frac{x}{y} = u \ \ \therefore \ x = uy
\text {Diff. } w. \ r. \ t. \ y
.\ .\ .\ \ \ \text {(2)}
\text {From (1), (2) and (3) we get, }
.\ .\ .\ \ \ \text {(3)}
\left( 1 + e^{ \frac{x}{y} } \right) \frac{dx}{dy} + e^{ \frac{x}{y} }\left( 1 - \frac{x}{y} \right) = 0
\left( 1 + e^u \right) \left( u + y \frac{du}{dy} \right) + e^u\left( 1 - u \right) = 0

---
u + y \frac{du}{dy} + u e^u + y e^u \frac{du}{dy} + e^u - u e^u = 0
u + y \frac{du}{dy} + y e^u \frac{du}{dy} + e^u = 0
u + e^u + y ( 1 + e^u ) \frac{du}{dy} = 0
( u + e^u ) dy + y ( 1 + e^u ) du = 0
\frac{dy}{y} + \frac{ (1 + e^u) du }{ u + e^u } = 0
\text {Dividing through out by } y ( u + e^u ) \text { we get,}
\int \frac{1}{y} \ dy + \int \frac{ 1 + e^u }{ u + e^u } \ du = 0
\text {Integrating through out, we get,}

---
\log y + \log ( u + e^u ) = \log c
.\ .\ . \ \text {[ From (2) ]}
\text {is the required general solution.}
\log ( yu + ye^u ) = \log c
yu + ye^u = c
x + ye^{ \frac{x}{y} } = c
\text {(vi). } x \frac{dy}{dx} - y + x \sin \left( \frac{y}{x} \right) = 0
.\ .\ .\ \ \ \text {(1)}
\therefore \ \ \frac{dy}{dx} = u + x \frac{du}{dx}
\text {Put } \frac{y}{x} = u \ \ \therefore \ y = ux
\text {Diff. } w. \ r. \ t. \ x
.\ .\ .\ \ \ \text {(2)}
\text {From (1), (2) and (3) we get, }
.\ .\ .\ \ \ \text {(3)}

---
x \left( u + x \frac{du}{dx} \right) - y + x \sin u = 0
ux + x^2 \frac{du}{dx} - ux + x \sin u = 0
x^2 \ du + x \sin u \ dx = 0
\text {Dividing through out by } x^2 \sin u \text { we get,}
\frac{du}{\sin u} + \frac{dx}{x} = 0
\int \frac{1}{\sin u} \ du + \int \frac{ 1 }{ x } \ dx = 0
\text {Integrating through out, we get,}
\int \text {cosec } u \ du + \int \frac{ 1 }{ x } \ dx = 0

---
\log ( \text {cosec }u - \text {cot }u ) + \log x = \log c
.\ .\ . \ \text {[ From (2) ]}
\text {is the required general solution.}
\log \left[ \ x \left( \frac{1}{ \sin u } - \frac{ \cos u }{ \sin u } \right) \ \right] = \log c
\frac{ x ( 1 - \cos u ) }{ \sin u } = c
x ( 1 - \cos u ) = c \sin u
\Rightarrow
x \left[ 1 - \cos \left( \frac{y}{x} \right) \right] = c \sin \left( \frac{y}{x} \right) \right]
\text {Solve the following differential equations .}
\text {(i) } \frac{dy}{dx} + \frac{y}{x} = x^2 - 3
\text {(2)}
\text {(iii) } ( x + a ) \frac{dy}{dx} - 3y = ( x + a )^5
\text {(ii) } ( x + 2y^3 ) \frac{dy}{dx} = y
\text {(iv) } ( 1 + x^2 ) \frac{dy}{dx} + y = e^{\tan ^{-1} x}

---
\text {(i). Given differential equation is , } \frac{dy}{dx} + \frac{y}{x} = x^2 - 3
\text {Solutions : }
\text {i.e. } \frac{dy}{dx} + \left( \frac{1}{x} \right) y = x^2 - 3,
\text {Which is of the form } \frac{dy}{dx} + Py = Q
\text {Where } P = \frac{1}{x} \text { and } Q = x^3 - 3
\text {Now, I.F. } = e^{\int P dx} = e^{ \int \frac{1}{x} dx} =
e^{ \log x} = x
\therefore \ \ \text { The general solution is }\ y.\text {( I.F. )} = \smallint Q \text {( I.F. )} dx
y.(x) = \smallint (x^3 - 3)x \ dx
= \smallint (x^4 - 3x) \ dx
xy = \frac{x^5}{5} - \frac{3x^2}{2} + c
\frac{x^5}{5} - \frac{3x^2}{2} - xy + c = 0
\text {is the required general solution.}

---
\text {(ii). Given differential equation is , } ( x + 2y^3 ) \frac{dy}{dx} = y
\text {i.e. } \frac{dy}{dx} = \frac{y}{x + 2y^3}
\text {Which is of the form } \frac{dx}{dy} + Px = Q
\text {Where } P = - \frac{1}{y} \text { and } Q = 2y^2
\text {Now, I.F. } = e^{\int P dy} = e^{ -\int \frac{1}{y} dy} =
e^{ - \log y} = e^{ \log y^{-1}} = y^{-1}
\therefore \ \ \text { The general solution is }\ x.\text {( I.F. )} = \smallint Q \text {( I.F. )} dy
\text {i.e. } \frac{dx}{dy} = \frac{x + 2y^3}{y}
\text {i.e. } \frac{dx}{dy} = \frac{x }{y} + 2y^2
\text {i.e. } \frac{dx}{dy} + \left( - \frac{1}{y} \right)x = 2y^2,
x.(y^{-1}) = \smallint (2y^2 )(y^{-1} \ dy
= \smallint 2y \ dy = 2. \frac{y^2}{2} + c
\frac{x}{y} = y^2 + c
\therefore \ \ x = y ( y^2 + c )
\text {is the required general solution.}

---
\text {(iii). Given differential equation is , } ( x + a ) \frac{dy}{dx} - 3y = ( x + a )^5
\text {i.e. } \frac{dy}{dx} - \frac{3y}{x + a}= ( x + a )^4
\text {Which is of the form } \frac{dy}{dx} + Py = Q
\text {Where } P = - \frac{3}{ x + a } \text { and } Q = ( x + a )^4
\text {i.e. } \frac{dy}{dx} + \left( - \frac{3}{x + a} \right) y = ( x + a )^4
\text {Now, I.F. } = e^{\int P dx} = e^{ \int - \frac{3}{ x + a } dy}
= e^{ -3 \int \frac{1}{ x + a } dy} =
= e^{ -3 \int \frac{1}{ x + a } dy} =
= e^{ -3 \log ( x + a ) }
= e^{ \log ( x + a )^{-3} }
= ( x + a )^{-3}

---
\text {is the required general solution.}
\therefore \ \ \text { I. F. } = ( x + a )^{-3}
\therefore \ \ \text { The general solution is }\ y.\text {( I.F. )} = \smallint Q \text {( I.F. )} dx
y.( x + a )^{-3} = \smallint ( x + a )^4( x + a )^{-3} \ dx
= \smallint ( x + a ) \ dx
\frac{y}{( x + a )^{3}} = \frac{( x + a )^{2}}{2} + c
2y = ( x + a )^5 + 2c( x + a )^{3}
\text {(iv). Given differential equation is , } ( 1 + x^2 ) \frac{dy}{dx} + y = e^{\tan ^{-1} x}
\text {i.e. } \frac{dy}{dx} + \frac{y}{1 + x^2}= \frac{ e^{\tan ^{-1} x}}{1 + x^2}
\text {Which is of the form } \frac{dy}{dx} + Py = Q
\text {i.e. } \frac{dy}{dx} + \left(\frac{1}{ 1 + x^2 } \right) y = \frac{ e^{\tan ^{-1} x}}{1 + x^2}

---
\text {Where } P = \frac{1}{ 1 + x^2 } \text { and } Q = \frac{ e^{\tan ^{-1} x}}{1 + x^2}
\text {Now, I.F. } = e^{\int P dx} = e^{ \int \frac{1}{1 + x^2} dx} =
\therefore \ \ \text { The general solution is }\ y.\text {( I.F. )} = \smallint Q \text {( I.F. )} dx
y.(e^{ \tan^{-1}x}) = \int \left( \frac{ e^{\tan ^{-1} x}}{1 + x^2} \right)(e^{ \tan^{-1}x}) \ dx
\text {is the required general solution.}
e^{ \tan^{-1}x}
= \int \frac{ e^{2\tan ^{-1} x}}{1 + x^2} \ dx
= \smallint e^{2t}\ dt
= \frac{e^{2t}}{2} + c
= \frac{e^{2\tan ^{-1} x}}{2} + c
y.e^{ \tan^{-1}x}
y = \frac{e^{\tan ^{-1} x}}{2} + \frac{c}{\tan ^{-1} x}}

---
\text {Find the equation of the curve passing through the point }
\text {(3).}
\text {Solutions : }
\left( \frac{3}{\sqrt{2}}, \sqrt{2} \right)
\text {having slope of the tangent to the curve at any point } ( x, y ) \text { is } - \frac{4x}{9y}
\text {Let P}=(x, y) \text { be any point on the curve. Slope of the tangent }
\text {to the curve at P is given by } \frac{dy}{dx} .
\text {According to the given condition } \ \frac{dy}{dx} = - \frac{4x}{9y}
\therefore \ \ \ 9y \ dy = - 4x \ dx
\text {i.e. } \ 4x \ dx + 9y \ dy = 0
\text {Integrating through out, we get,}
\smallint 4x \ dx + \smallint 9y \ dy = 0
\frac{4x^2}{2} + \frac{9y^2}{2} = \frac{c}{2}
\Rightarrow \ \ 4x^2 + 9y^2 = c
.\ .\ .\ \ \ \text {(1)}

---
\text {Given that the curve is passing through the point }
\left( \frac{3}{\sqrt{2}}, \sqrt{2} \right)
4\left( \frac{3}{\sqrt{2}} \right)^2 + 9\left( \sqrt{2} \right)^2 = c
\text {Put } x = \frac{3}{\sqrt{2}} \text { and } y = \sqrt{2} \text { in (1) we get,}
4\left( \frac{9}{2} \right) + 9\left( 2 \right) = c
\Rightarrow
c = 36
\Rightarrow
\text {Put } \ c = 36 \ \ \text { in (1) we get,}
4x^2 + 9y^2 = 36
\text {is the required equation of the curve.}
\text {The curve passes through the point }(0, 2). \text {The sum of the co-ordinates}
\text {(4).}
\text {Solutions : }
\text {of any point on the curve exceeds the slope of the tangent to the curve}
\text {at that point by 5. Find the equation of the curve.}
\text {Let P}=(x, y) \text { be any point on the curve. Slope of the tangent }
\text {to the curve at P is given by } \frac{dy}{dx} .

---
\text {According to the given condition, } \ \ x + y = \frac{dy}{dx} + 5
\text {i.e. } \ \ \frac{dy}{dx} - y = x - 5
\text {i.e. } \ \ \frac{dy}{dx} + ( - 1 ) y = x - 5
\text {Which is a linear differential equation of the form } \frac{dy}{dx} + Py = Q
\text {Where } P = - 1 \text { and } Q = x - 5
\therefore \ \ \text { The general solution is }\ y.\text {( I.F. )} = \smallint Q \text {( I.F. )} dx
\text {Now, I.F. } = e^{\int P dx} = e^{ - \int dx} = e^{ - x }
y.( e^{ - x } ) = \smallint ( x - 5 ) ( e^{ - x } ) dx
= ( x - 5 ) \smallint e^{ - x } dx - \int \left( \smallint e^{ - x } dx. \frac{d}{dx}( x - 5 ) \right) dx

---
y.( e^{ - x } ) = ( x - 5 ) \ \frac{e^{ - x }}{-1} - \int \left( \frac{e^{ - x }}{-1}. ( 1 ) \right) dx + c_1
= - \frac{ x - 5 }{e^x} + \int e^{ - x } dx
= - \frac{ x - 5 }{e^x} + \frac{e^{ - x }}{-1} + c_1 + c_2
y.( e^{ - x } ) = - \frac{ x - 5 }{e^x} - \frac{1}{e^{ x }} + c_1 + c_2
\text {Multiplying through out by } e^x \text { we get,}
y \ = - ( x - 5 ) - 1 + ( c_1 + c_2 ) e^x
y \ = - x + 5 - 1 + c. e^x
y \ = 4 - x + c. e^x
.\ .\ .\ \ \ \text {(1)}
\text {where } c = c_1 + c_2

---
######	DONE	######
\text {Given that the curve is passing through the point } (0, 2)
\text {Put } x = 0 \text { and } y = 2 \text { in (1) we get,}
2 \ = 4 - 0 + c. e^0 \ \ \Rightarrow \ \ c = - 2
\text {Put } \ c = - 2 \ \ \text { in (1) we get,}
y \ = 4 - x - 2 e^x
\text {is the required equation of the curve.}

---
T H A N K Y O U

---
This is a presentation in
LI	BRE OFFICE – IMPRESS
By
Mr. Prahlad Chippalagtti.